For imx6 linux BSP porting:-

=> In the u-boot source code, you make compilation.
export ARCH=arm // arm architecture

=> set freescale cross compiler path
export CROSS_COMPILE = //path to toolchain

=> select the board file
make <board>_config	// mention the board name, this config file is there in	include/configs/mx6sabresd.h Cross check seted config file in include/config.h

=> make

Note:-
    1. u-boot level IOMUX configuration did in board/freescale/sabresd/mx6sabresd.c
    2. Boot args mentioned in include/configs/mx6sabresd.h
    3. DDR value update in plugin.S inside board file Dir.

About Boot Argument:-

=> baudrate is 115200

=> console is ttymxcX
Note:- Check in schmatic debug port connected UART port (ie:UART1=ttymxc0) If it's wrong log stoped in starting kernel.

=> After uboot complition, it goes to bootcmd – there we mention run bootcmd_mmc. In this name have everything to load uImage and dtb(kervel version above 3.14.x). And run loaded address.

=> In this bootcmd_mmc include baudrate,console and rootfs details.

Note:-
1) Both uimage, dtb is readed but i will stoped in starting kernel. Two issue is there.

=> console is wrong (ttymxc0)

=> Otherwise both image reading address may be conflict. Change the address of the image.And cross check with this size, It enough or not.

2) HDMI interface if you use, mention resolutions and other details near to rootfs details.

Kernel Compilation:-

=> In the u-boot source code, you make compilation.
export ARCH=arm // arm architecture

=> set freescale cross compiler path
export CROSS_COMPILE = //path to toolchain

=> select the board file
make <board>_defconfig	// mention the board name, this config file is there in	arch/arm/configs/mx6sabresd_defconfig

=> make;make uImage LOADADDR=0x12700000

=> make imx6q-sabresd.dtb

Note:-
    1. If u made any changes in make menuconfig, cp .config to defconfig file.
    2. IOMUX config did in arch/arm/boot/dts/imx6q-sabresd.dts